# CAN Messages

CAN ID 0x351 (send 1/sec) Limits
Byte		Unit	Scale
1	Charge Voltage High Byte	V	0,1
2	Charge Voltage Low Byte
3	Charge Current High Byte	A	0,1
4	Charge Current Low Byte
5	Discharge Current High Byte	A	0,1
6	Discharge Current Low Byte
7	Discharge Voltage High Byte	V	0,1
8	Discharge Voltage Low Byte

CAN ID 0X355 (send 1/sec) SOC / SOH
Byte		Unit	Scale
1	SOC LowByte	%	1
2	SOC HighByte
3	SOH LowByte	%	1
4	SOH HighByte
5	SOC LowByte	%	0,1
6	SOC HighByte
7
8

CAN ID 0X356 (send 1/sec) Status
Byte		Unit	Scale
1	Pack Voltage LowByte	V	0,01
2	Pack Voltage HighByte
3	Current LowByte	A	0,1
4	Current HighByte
5	Av. Temperature LowByte	°C	0,1
6	Av. Temperature HighByte
7	-
8	-

CAN ID 0X35A (send 1/sec) Warnings / Alarms
Byte		Unit	Scale
1	alarm[0]		0 = OK, 1=Error
2	alarm[1]
3	alarm[2]
4	alarm[3]
5	warning[0]		0 = OK, 1=Error
6	warning[1]
7	warning[2]
8	warning[3]

Bit	alarm[0]	alarm[1]	alarm[2]	alarm[3]
1	-	Under Temperature	-	Cell Imbalance
2	-	-	-	-
3	Cell Over Voltage	-	-	-
4	-	-	-	-
5	Cell Low Voltage	-	-	-
6	-	-	-	-
7	Over Temperature	-	-	-
8	-	-	-	-

Bit	warning[0]	warning[1]	warning[2]	warning[3]
1	-	Under Temperature	-	-
2	-	-	-	-
3	Cell Over Voltage	-	-	-
4	-	-	-	-
5	Cell Low Voltage	-	-	-
6	-	-	-	-
7	Over Temperature	-	-	-
8	-	-	-	-

CAN ID 0X372 (send 1/sec) Number of Modules
Byte		Unit	Scale
1	Number of Modules LowByte
2	Number of Modules HighByte

CAN ID 0X373 (send 1/sec) Extreme Values
Byte		Unit	Scale
1	Low Cell Volt LowByte	V
2	Low Cell Volt HighByte
3	High Cell Volt LowByte	V
4	High Cell Volt HighByte
5	Low Temp. LowByte	K
6	Low Temp. HighByte
7	High Temp. LowByte	K
8	High Temp. HighByte

CAN ID 0X372 (send 1/sec) Installed Capacity
Byte		Unit	Scale
1	Installed Capacity LowByte	Ah
2	Installed Capacity HighByte

Plug		BMS		C
Plug connect
	AC conn / A max (contin.) →
		Chk Cond. / stat Charge
	← Charge start
Close lock / Chk Lock? / charge en.
	Status →
		Chk Stat.
			Charge start / A max →
	← Charge stop		Charge stop / A max = 0 →
Vehicle detec. / Unlock?

Plug unconn.	Status (contin.) →	Chk if pres. / Else → Err.

CAN Plug:
AC conn, Amax,

Status	Red LED	Green LED
norm	off	off
Plug connected	Blink slow	off
Charging / locked	on	Blink slow
Charged / locked	on	on
error	Blink fast	off